## 2017 Honda Fit Specifications and Features

| ENGINEERING | LX | EX |
| --- | --- | --- |
| Engine Type | In-Line 4-Cylinder | In-Line 4-Cylinder |
| Engine Block/Cylinder Head | Aluminum-Alloy | Aluminum-Alloy |
| Displacement (cc) | 1498 | 1498 |
| Horsepower @ rpm (SAE net) | 130 @ 6600 | 130 @ 6600 |
| Torque (lb-ft @ rpm, SAE net) | 114 @ 4600 | 114 @ 4600 |
| Redline (rpm) | 6800 | 6800 |
| Bore and Stroke (mm) | 73 x 89.5 | 73 x 89.5 |
| Compression Ratio | 11.5:1 | 11.5:1 |
| Valve Train | 16-Valve DOHC i-VTEC® | 16-Valve DOHC i-VTEC® |
| Fuel Injection | Direct | Direct |
| Drive-by-Wire Throttle System | • | • |
| Eco Assist™ System | CVT | CVT |
| CARB Emissions Rating1 | LEV3-ULEV125 | LEV3-ULEV125 |
| Direct Ignition System with Immobilizer | • | • |
| 100K +/- Miles No Scheduled Tune-Ups2 | • | • |
| TRANSMISSIONS | LX | EX |
| 6-Speed Manual Transmission | • | • |
| Gear Ratios: 1st: 3.461, 2nd: 1.869, 3rd: 1.235, 4th: 0.948, 5th: 0.809, 6th:0.727, Reverse: 3.307, Final Drive Ratio: 4.62 |  |  |
| Continuously Variable Transmission (CVT) with Sport Mode | Available | with Dual-Mode Paddle Shifters (Available) |
| Gear Ratios: 2.526～0.408, Reverse:2.706～1.382, Final Drive: 5.44 |  |  |
| BODY/SUSPENSION/CHASSIS | LX | EX |  |
| Unit-Body Construction | • | • |  |
| MacPherson Strut Front Suspension | • | • |  |
| Torsion-Beam Rear Suspension | • | • |  |
| Stabilizer Bar (mm, front) | 25.4 | 25.4 |  |
| Electric Power-Assisted Rack-and-Pinion Steering (EPS) | • | • |  |
| Steering Wheel Turns, Lock-to-Lock | 2.51 | 2.51 |  |
| Steering Ratio | 13.06 | 13.06 |  |
| Turning Diameter, Curb-to-Curb (ft) | 35.1 | 35.1 |  |
| Power-Assisted Ventilated Front Disc/Rear Drum Brakes (in, front/rear) | 10.3 / 7.9 | 10.3 / 7.9 |  |
| Wheels | 15" w/Full Covers | 16" Alloy |  |
| All-Season Tires | 185 / 60 R15 84T | 185 / 55 R16 83H |  |
| Compact Spare Tire | T135 / 80 D15 99M | 135 / 80 D15 99M |  |
| EXTERIOR MEASUREMENTS | LX | EX |
| Wheelbase (in) | 99.6 | 99.6 |
| Length (in) | 160.0 | 160.0 |
| Height (in) | 60.0 | 60.0 |
| Width (in) | 67.0 | 67.0 |
| Track (in, front/rear) | 58.3 / 58.0 | 58.1 / 57.7 |
| Curb Weight (lbs, MT/AT) | 2513 / 2544 | 2573 / 2630 |
| Weight Distribution (%, front/rear, MT) | 61 / 39 | 60 / 40 |
| Weight Distribution (%, front/rear, AT) | 62 / 38 | 61 / 39 |
| INTERIOR MEASUREMENTS | LX | EX |
| Headroom (in, front/rear) | 39.5 / 37.5 | 38.0 / 37.6 |
| Legroom (in, front/rear) | 41.4 / 39.3 | 41.4 / 39.3 |
| Shoulder Room (in, front/rear) | 54.8 / 52.6 | 54.8 / 52.6 |
| Hiproom (in, front/rear) | 51.5 / 45.1 | 51.5 / 45.1 |
| Cargo Volume (cu ft, seat up/down) | 16.6 / 52.7 | 16.6 / 52.7 |
| Passenger Volume (cu ft) | 95.7 | 93.8 |
| Seating Capacity | 5 | 5 |
| EPA MILEAGE RATINGS3/FUEL | LX | EX |
| 6-Speed Manual (City/Highway/Combined) | 29/36/32 | 29/36/32 |
| Fuel (gal) | 10.6 | 10.6 |
| Required Fuel | Regular Unleaded | Regular Unleaded |
| ACTIVE SAFETY | LX | EX |
| Vehicle Stability Assist™ (VSA®) with Traction Control4 | • | • |
| Anti-Lock Braking System (ABS) | • | • |
| Electronic Brake Distribution (EBD) | • | • |
| Brake Assist | • | • |
| Tire Pressure Monitoring System (TPMS)5 | • | • |
| Daytime Running Lights (DRL) | • | • |
| PASSIVE SAFETY | LX | EX |
| Advanced Compatibility Engineering™ (ACE™) Body Structure | • | • |
| Dual-Stage, Multiple-Threshold Front Airbags (SRS) | • | • |
| SmartVent® Front Side Airbags | • | • |
| Side Curtain Airbags with Rollover Sensor | • | • |
| 3-Point Seat Belts at all Seating Positions | • | • |
| Front 3-Point Seat Belts with Automatic Tensioning System | • | • |
| Lower Anchors and Tethers for CHildren (LATCH): Lower Anchors (2nd-Row Outboard), Tether Anchors (2nd-Row All) | • | • |
| Driver's and Front Passenger's Seat-Belt Reminder | • | • |
| Child-Proof Rear Door Locks | • | • |
| EXTERIOR FEATURES | LX | EX |
| One-Touch Power Moonroof with Tilt Feature |  | • |
| Roof-Mounted Antenna | • | • |
| Security System with Remote Entry | • | • |
| Smart Entry System |  | • |
| One-Touch Turn Indicators | • | • |
| 2-Speed/Intermittent Windshield Wipers | • | • |
| Intermittent Rear Window Wiper/Washer | • | • |
| Body-Colored Rear Roofline Spoiler | • | • |
| Multi-Reflector Halogen Headlights with Auto-On/Off | • | • |
| Fog Lights |  | • |
| LED Brake Lights | • | • |
| Body-Colored, Power Side Mirrors | • | • |
| COMFORT & CONVENIENCE | LX | EX |
| Air Conditioning with Air-Filtration System | • | • |
| Multi-Angle Rearview Camera | with Guidelines | with Dynamic Guidelines |
| Honda LaneWatch™6 |  | • |
| Bluetooth® HandsFreeLink®7 | • | • |
| SMS Text Message Function8 |  | • |
| Push Button Start |  | • |
| Power Windows with Auto-Up/Down Driver's Window | • | • |
| Power Door Locks/Programmable Auto-Locking Doors | • | • |
| Illuminated Driver's Window and Door Lock Controls | • | • |
| Cruise Control | • | • |
| Illuminated Steering Wheel-Mounted Controls | Cruise / Audio / Phone | Cruise / Audio / Phone |
| Tilt and Telescopic Steering Column | • | • |
| Center Console with Armrest and Storage Compartment | • | • |
| Beverage Holders | • | • |
| Driver's and Front Passenger's Vanity Mirrors | • | • |
| Map Lights | • | • |
| 12-Volt Power Outlets (front/center console) | • | • |
| HDMI Port |  | • |
| Passenger-Side Seatback Pocket | • | • |
| Remote Fuel Filler Door Release | • | • |
| Cargo Area Tie-Down Anchors |  | • |
| Rear Window Defroster | • | • |
| Cargo Area Light | • | • |
| Floor Mats |  | • |
| Door-Pocket Storage Bins (front/rear) | • | • |
| SEATING | LX | EX |
| Driver's Seat with Manual Height Adjustment | • | • |
| Adjustable Front Seat-Belt Anchors | • | • |
| Adjustable Head Restraints | • | • |
| 60/40 Split 2nd-Row Magic Seat® | • | • |
| AUDIO SYSTEMS | LX | EX |
| 180-Watt AM/FM/CD Audio System with 6 Speakers |  | • |
| 5" Color LCD Screen | • |  |
| 7" Display Audio with High-Resolution WVGA (800x480) Electrostatic Touch-Screen and Customizable Feature Settings |  | • |
| HondaLink™ Next Generation10 |  | • |
| Pandora®13 Compatibility |  | • |
| Bluetooth® Streaming Audio | • | • |
| Display Audio Interface14 |  | • |
| USB Audio Interface15 | Front | Front & Center Console |
| MP3/Auxiliary Input Jack | • |  |
| MP3/Windows Media®16 Audio (WMA) Playback Capability | • | • |
| Radio Data System (RDS) | • | • |
| Speed-Sensitive Volume Control (SVC) | • | • |
| INFORMATION DISPLAY | LX | EX |
| Average Fuel Economy Indicators | • | • |
| Clock | • | • |
| Digital Odometer and Digital Trip Meters (2) | • | • |
| Engine Oil Life Indicator | • | • |
| Exterior Temperature Indicator | • | • |
| Instant Fuel Economy Indicator | • | • |
| Miles-to-Empty Indicator | • | • |
| INSTRUMENTATION | LX | EX |
| 12-Volt Battery-Charging System Indicator | • | • |
| ABS Indicator | • | • |
| Airbag System Indicator | • | • |
| Backlit Gauges | • | • |
| Brake System Indicator | • | • |
| Coolant Temperature Indicator | • | • |
| Cruise Control Indicators | • | • |
| Door- and Hatch-Open Indicator | • | • |
| Electric Power Steering (EPS) Indicator | • | • |
| Fog Lights Indicator |  | • |
| Fuel Level Indicator | • | • |
| Headlights-On Indicator | • | • |
| High-Beam Indicator | • | • |
| Immobilizer System Indicator | • | • |
| Low-Brake Fluid Indicator | • | • |
| Low-Tire Pressure Indicator | • | • |
| Low-Fuel Indicator | • | • |
| Low-Oil Pressure Indicator | • | • |
| Maintenance Minder™ Indicator | • | • |
| Malfunction Indicator | • | • |
| Seat-Belt Reminder Indicator | • | • |
| Smart Entry System Indicator |  | • |
| Starter System Indicator |  | • |
| Tachometer | • | • |
| TPMS Indicator | • | • |
| VSA System and VSA-Off Indicators | • | • |